## Slide 1: ALPINE HONDA 2Wheel POC Q&A (06/03)
Questions about A&W CP/AA & BT Stack for ALPINE
Q1: Availability and supportability of the BLE beacon function
A1: A&W can support
Q2: The number of BLE connections that can be supported simultaneously and any constraints related to Advertising operation
A2: Determined by the controller, the Host Stack can support any number of hosts.
Q3: Whether transmission interval and transmission power can be controlled
A3: Yes, extended advertising can control these two variables.
Q4: The impact of beacon transmission on system load and power consumption
A4: Advertising does not consume host CPU; its power consumption depends on the interval and transmission power. ALPINE can inquire with the controller manufacturer about this.
Q5: Availability of support for Apple Find My network (MFi)
A5: A&W can support development, but manufacturers need to obtain an MFi token from Apple.

## Slide 2: ALPINE HONDA 2Wheel POC Q&A (06/03)
Questions about A&W CP/AA & BT Stack for ALPINE
Q6: Availability of support for Google Find My Device Network
A6: A&W can support development, similar to Apple, but manufacturers need to apply for a key from Google.
Q7: Additional hardware and/or software requirements necessary for each support option
A7: Secure Storage is needed to store the Token and Key.
Q8: Expected costs and schedule impacts associated with certification acquisition
A8: If for Bluetooth SIG certification, A&W provides Stack DID and Profile Package DID.
AlpsAlpine only needs to combine the two A&W DIDs plus the HW DID to apply for the End Product DID.
The only cost is the fee for applying for the End Product DID.
Q9: Any impact on mass production and long-term supply
A9: After mass production A&W will continue to support the project
Q10: Regarding CV regulations(USA Connected Regulations) How can A&W prove that we do not violate CV regulations? (e.g., SBOM)
A10: We will provide a complete Software Bill of Materials (SBOM) for our delivered libraries. A&W is a Taiwanese company. All software is entirely developed in-house by our internal team. Any declaration documents from the customer will be signed after internal review and mutual agreement.

## Slide 3: ALPINE HONDA 2Wheel POC Q&A (06/03)
Questions about A&W CP/AA & BT Stack for ALPINE
Q11: Please answer the problems and challenges in the concept of transmitting CP/AA sound to the headset via BT.
A11: Audio routing creates latency, adding 200-300ms for A2DP and 100-200ms for HFP (jitter buffer is needed). Switching use cases between A2DP and HFP may causes audio gap. To avoid 2.4GHz RF interference, Wi-Fi must strictly use the 5GHz band, especially for Android Auto. Non-standard audio path risks failing strict Apple MFi and Google GAL acoustic certifications.
Q12: Will the estimate change due to the BT 2-chip configuration?
(This time, in addition to the WiFi/BT module, there is 2-chip control of the Stack-embedded BT Chip for channel sounding support)
A12: No change , because the second chip use complete type for channel sounding , the chip include stack/profile .
if our understanding is correct .
Q13: The estimate will not change even if Apple Find My Network (MFi) and Google Find My Device Network specifications are added (Need to added to the estimate?)
A13: Yes
Q14: The formal estimate for A&W BT Stack and BT Stack + CP/AA differs from the quantity conditions requested by ALAP, so correction and resubmission are necessary.
A14: A&W revised the quote.

## Slide 4: ALPINE HONDA 2Wheel POC Q&A (06/15)
Questions about A&W CP/AA & BT Stack for ALPINE
Q15: ALAP have one concern regarding Apple/Google Find My.
The quote states that ALAP will provide the specifications. Wouldn't this fall under the NRE (Network Research Engineer) category?
A15: For Apple/Google Find My Device integration, it needs AlpsAlpine to provide the 'Token and Key' for A&W to do functional verification.
Q16: “ALPSALPINE Electronics shall provide A&W with the latest CarPlay and Android Auto libraries, along with the relevant documentation and test specifications.” ALAP's concerns stemmed from the wording in the above quotation.
If it's true that "Find Me documentation is not required and only the token and key need to be provided," then the above wording should be slightly revised.
A16: According to Apple and Google rules, it is product owner (Honda or AlpsAlpine) to get Plug-In SDK from Apple and Google for A&W to do final integration. Apple/Google Find My: AlpsAlpine only needs to supply the 'Token and Key' to A&W for functional verification
Q17: Regarding Apple/Google Find My, do you have any information on how long the development is expected to take?
(Our customer are interested in knowing the impact.)
A17: Apple/Google Find My development is estimated at 6–8 weeks, including functional verification.

## Slide 5: ALPINE HONDA 2Wheel POC Q&A (06/17)
Questions about A&W CP/AA & BT Stack for ALPINE
Q18: Based on ALAP's experience, we have never developed in the way you described. It's Apple → 3rd Party → ALAP.
If ALAP accept this flow, I think it would still be NRE development.
It would seem like development would be based on "input from ALAP."
By the way, I'm assuming A&W has an Apple Developer license, correct?
(Even without input from ALAP, can A&W obtain what it needs from Apple and start development?)
A18: 1. Yes, A&W is Apple Developer.
2. Development : A&W can develop, integrate, test CarPlay for ALAP's system, no need to acquire anything in advance.
3. Final Release:According to Apple's rule we know, it is product owner (Honda ?) to get Plug-In SDK from Apple for final release.
Developer (A&W) has no right to use our own version for shipping.
Q19: ALAP are currently discussing this using Linux as the operating system, but do you have any suggestions for an RTOS (Real-Time OS)?
Background of the question:In addition to our current hardware configuration, we are beginning to consider alternative hardware
configurations from a cost perspective.
The constraint is that the assumed OS will change as described above.
A19: 1. The SOC system must be CarPlay compliant.
2. The information we got is, NXP 2770 is prepaing for CarPlay, but not yet to be ready.
It is no problem for A&W to port CarPlay to a CarPlay ready RTOS system.

## Slide 6: ALPINE HONDA 2Wheel POC Q&A (06/18)
Questions about A&W CP/AA & BT Stack for ALPINE
Q20: > There is no problem for A&W to port CarPlay to a CarPlay-ready RTOS system.
Just to confirm, is it correct to assume that you can also provide a Bluetooth stack for RTOS?
A20: A&W has very good reputation for its RTOS BT STACK, very high quality with low RAM/ROM size.
Q21: Regardless of whether Q20 is possible or not, please let us know if there are any impacts such as changes to the quotation conditions.
A21: no impact on the quotation

## Slide 7: ALPINE HONDA 2Wheel POC Q&A (07/08)
Questions about A&W CP/AA & BT Stack for ALPINE
Q22: Regarding the software block diagram in the attached document, the areas excluding Bluetooth, Wi-Fi, CarPlay/Android Auto, and the Meter HMI fall within A&W's development scope.
ALAP would like to reconfirm whether it is possible to outsource the development of these areas to A&W and request a cost estimate for doing so.
A22:
Q23: ALAP would like to confirm details regarding the CP/AA stack.
ALAP understand that audio and video codecs are required to implement CP/AA.
Are the codecs not included in the Telechips BSP provided within your company's stack?
Please let me know which codecs are included in your stack.
The reason for this inquiry is that certain codecs may incur licensing or patent-related fees, and we wish to factor these costs into our estimates beforehand.
ALAP are particularly interested in the following codecs:
>Opus
>H.264/MPEG-4 AVC decoder
>H.265
A23: